## Slide 1: Lecture 18 – Designing a processor
2018.02.19
Details are not the details.
They make the design.
– Charles Eames

## Slide 2: Assignments
Today’s material is from chapter 6
HW05 due Thursday
Lab 06 due this week

## Slide 3: Lectures 18 – Designing a processor
2018.02.19
King: Young Lady, look along the road and tell me if you can see either of my messengers.
Alice: I see nobody on the road.
King: I only wish I had such eyes. To see Nobody, at such a distance, too! It's enough for me to see real people by this light.
from Through the Looking-Glass, and What Alice Found There
by Lewis Carroll (Charles Lutwidge Dodgson), 1871.

## Slide 4: About the details of seeing Nobody in CS
Running a program is a complicated business
Abstraction hides detail and helps understand a chosen level of the computational platform
  Example: a typical C program abstracts (hides) the majority of its code using the #include mechanism
  To know program function and limitations also requires knowing the library functions called
Abstraction, yes; but details always matter
Pay attention to hidden information about bus size, control signals, and data type conversion in Fig. 6.9
Be able to see Nobody, be able to see hidden detail

## Slide 5: Build processor control – decode instr.
Decoding an instruction means to
  Interpret all fields of instruction format and
  Control the data path – generate logic signals to tell the data path circuit what to do
A well-chosen instruction format makes decoding cheaper and faster (simpler circuit)
Very easy decoding for our textbook example, just partition the 32 wires carrying the instruction bit string

## Slide 6: Decode for the example processor
32-bit string from Instruction Memory Data Out wires is decoded by grouping wires according to the instruction format fields.
Most instruction sets are more complex to decode.
Wire group functions are:
• Pointing to a memory location (3 instances, 4 bits each) • Value delivery (15 bits) • Selection of operation within arithmetic/logic unit (ALU) circuit (another pointer, 5 bits)
32
/
32
/
32
/
32
/
Address, or pointer
Pointer
Constant
Pointer, or address
32
/
Instruction
/
5
15
/
4
/
4
/
4
/
Control, selects operation (points)
Value, constant
Pointer
Pointer
Pointer

## Slide 7: Time to: 2) Locate and read operands
Instr. memory provides one instruction per fetch
Execution of this ISA needs up to three memory accesses: 2 operands (reads) and 1 result (write)
For speed of execution, want execution memory to support three, independent simultaneous accesses; but it need not be a large number of locations
Today’s technology’s solution is the register unit, a.k.a. the register file
  A small collection of registers, each register sized to hold the bit string of a default-size number or a default-size memory address

## Slide 8: Time to: 2) Locate and read operands
Which fields are operands?
Operands in the instruction format are
  reg A, reg B, and offset which are, respectively
  pointer, pointer, and immediate value
What to do with pointer bit strings?
  Send the 2 pointers to address inputs of register unit (file)
  Register file outputs copies of the bit strings that are g being stored in the two registers pointed to
Immediate value bit string is sent directly to the ALU

## Slide 9: Register Unit (register file) ckt. details
Contains sixteen 32-bit registers
Inputs: 45 wires, as follows
  [12 bits] Three 4-bit addresses because one instr. may access reg_A, reg_B, and dst_reg
  [32 bits] Result value to be written into dst_reg
  [1 bit] Not every instruction uses dst_reg, so a Write_Enable control signal input for the Register File (abstracted out, not shown in textbook figures) is necessary to enable/disable storing (writing) a result
Outputs: 64 wires
  Copies of the 32-bit contents of any 2 of 16 registers, including ability to duplicate contents of one register to both outputs

## Slide 10: Read operands, completing Fetch
15-bit value direct to ALU
5 bits of control signals (pointer) direct to ALU
Copy of
Notes: Use thought question #1, #2, #3, and #4 here.

## Slide 11: Time to: 3) Execute instruction
Execution circuit (ALU) supports all instructions
Instr Definition add contents[dst_reg]← cont[reg_A]+c[reg_B] load c[dst_reg]←Data_Memory[offset +c[reg_A]] store Data_Memory[offset + reg_A] ← reg_B jump Fetch at Instr_Memory[offset + reg_A]
What does each instruction ask of the ALU?
  add: add values sourced from reg_A and reg_B
  load: add offset and contents of reg_A
  store: add offset and contents of reg_A
  jump: add offset and contents of reg_A
ALU must perform integer add for all 4 ISA instr.

## Slide 12: Design ALU input (operands) circuit
Textbook author’s design choice is to implement add Offset and value sourced from Reg ? as Offset + reg_A
  Could have chosen Offset + reg_B

## Slide 13: Design ALU input (operands) circuit
Design question #1: How should we build the circuit so that ADD instr. sends reg_A and reg_B to the ALU, while LOAD/STORE/JUMP send reg_A and Offset to ALU?
  Answer: Use a MUX to select Offset or reg B as needed
Design question #2: How do we match the 15-bit offset representation to the 32-bit ALU?
  Answer: Increase the 15-bit size of the 2’s complement Offset to 32 bits using sign extension

## Slide 14: Arithmetic/Logic Unit (ALU) in action
reg A 32-bit value
reg B 32-bits
Sign extend
Selected operand
32-bit sign extended offset value in 2’s comp
15 bit offset in 2’s comp
Mux circuit chooses 1 of 21 inputs to connect to ALU. Mux must receive a 1-bit signal controlling which 1 of 21 inputs is selected. Mux control input wire (1-bit pointer to sign-extended offset or to reg B) is abstracted out of diagram.
Opcode bits to control ALU

## Slide 15: ALU has produced a result; what next?

## Slide 16: Time to: 4) Write result into specified location
What are the results and where do they go?
  ADD: ALU output is the result, deliver to dst_reg
  JUMP: ALU output is next_instr_ptr, deliver to pgm. ctr. (current_instr_ptr register)
  LOAD: ALU output is pointer that must be sent to data memory, which then produces copy of the location contents which, finally, must be written into dst_reg
  STORE: ALU output is pointer that must be sent to data memory along with the value from reg_B to be written into the data memory location

## Slide 17: Put ADD result where it belongs
ADD result data path
  ADD: ALU output is the result, deliver to dst_reg. Result has the meaning “integer” because it comes from the integer adder output. However, looking at the voltages on the data path (bus) wires is insufficient to determine whether the integer has unsigned or 2’s representation because the adder circuit works with both formats.

## Slide 18: Put LOAD result where it belongs
LOAD result data path
  LOAD: ALU output is pointer sent to data memory, which then produces a copy of the location contents which, finally, must be written into dst_reg; Result is a bit string from memory: no inherent meaning at this level of abstraction. Meaning is imposed at a higher level by the software.

## Slide 19: Put STORE result where it belongs
STORE result data path
  STORE: ALU output is pointer sent to data memory along with the value from reg B to be written into the data memory location. Result is a bit string from reg_B written in memory, where it has no inherent meaning.

## Slide 20: Put JUMP result where it belongs
JUMP result data path
  JUMP: ALU output is a computed Next_instruction_pointer, must deliver to Instruction_pointer_register. Result meaning is location of next instruction on the run-time execution path.

## Slide 21: Result: Default_next_instruction_pointer
  Default_next_instruction_pointer is computed after every fetch because it is likely to be needed. Result meaning is location of sequentially_next instruction.
Default_next_instruction_pointer

## Slide 22: All result paths, overlapped
ADD result data path
JUMP result data path
LOAD result data path
STORE result data path
  Input choices by Mux M3 and Mux M1 control where ADD, LOAD, and JUMP results are delivered (Mux control abstracted)

## Slide 23: Figure 6.9 is fundamental
Learn the function of each wire and device, the number of bits anywhere, the data type of every bit string, and the operation of abstracted control circuitry and you will know the central processing unit (CPU) of a computer

## Slide 24: Summary
A circuit that can fetch and execute instructions is programmable
The bits in machine code instructions control the operation of the data path; not all instruction format bit positions contain information for every instruction
Multiplexers route bits traveling on buses from hardware units to a hardware unit
Meaning of bits is set by the hardware unit (1) receiving the bits or (2) computing the bits

## Slide 25: Lecture 19 – More speed using pipelining
2018.02.21
I feel the need – the need for speed!
– Lt. Pete “Maverick” Mitchell and Lt.(jg) Nick “Goose” Bradshaw
in the movie Top Gun

## Slide 26: Assignment for today
Covering chapter 5.13 through 5.17 from the hardware perspective
Read chapter 7 and 8

## Slide 27: Announcements
HW05 due Thursday
Lab 06 due this week

## Slide 28: Look for steps within fetch-execute cycle
Observe signals as they propagate through the processor circuit.
Look for a sequence of simple actions that execute an instruction.

## Slide 29: 1) Fetch an instruction and compute the Default_Next_Instruction_Pointer
  Fetch done using Current_Instruction_Pointer, also known as (a.k.a.) the Program Counter
Fetched
instruction
Current_Instruction_Pointer 
 Default_Next_ Instruction_Pointer

## Slide 30: 1) Fetch, 2) Decode instr., access operands, and sign extend offset
  Decode, point to, and access registers and sign extend offset. All of this is performed by the circuit regardless of opcode.
Sign extend

## Slide 31: 1) Fetch, 2) Decode, 3) Execute instr.
  ALU and M2 control inputs are functions of Opcode field bits
Sign extend

## Slide 32: Fetch, Decode, Ex, 4) access Data Mem
  Data Memory (DM) always receives Addr._In and Data_In bit strings. READ_Enable (RE) & WRITE_Enable (WE) DM controls are functions of Opcode. DM reads at Addr._In if RE = true, writes Reg_B_Value at Addr._IN if WE = true, and does nothing if RE = WE = false.
Sign extend

## Slide 33: Fetch, Decode, Ex, Mem, 5) Write Back
  Bit strings from all sources of results are routed by M3 and M1 to the appropriate destination register (32-bit pgm. ctr. is a register). M3 and M1 control signals are functions of the Opcode.
Sign extend

## Slide 34: Clock rate and instruction rate
The pace of the processor Fetch-Execute cycle is set by a clock signal
Number of clock cycles necessary to Fetch and Execute an instruction and the clock cycle frequency depends on
  Processor circuit design (not pipelined, pipelined)
  Specific instruction to be executed
  ALU circuit design (“better” circuit design has a smaller worst case propagation delay)
  Speed of memory technology storing operand(s) and result (may be slower than processor circuit)

## Slide 35: One-instruction-per-clock-cycle design
Sign extend
The only clocked device,
the PC register
Clock
Circuitry put into action by current instruction bits
Long signal paths imply long propagation time, implies long wait for current instruction to complete fetch-execute, implies a long wait until the circuit can fetch the next instruction

## Slide 36: Processor design criteria
Designs should be evaluated against a set of criteria important for the given user, e.g.,
  Software compatibility
  Performance
  Price
  Power consumption
  …
Which criteria are common to most users?
  After primary concerns of software compatibility, users often care next most about performance
Much effort in computer architecture focused on performance and power consumption

## Slide 37: Example: time to do laundry
Assume you have:
  One washer (takes 30 minutes)
  One drier (takes 40 minutes)
  One “folder” (takes 20 minutes)
Takes 90 minutes to wash, dry, and fold 1 load of laundry.
  How long does it take to do 4 loads?

## Slide 38: One-load-at-a-time process (sequential)
4 loads done sequentially takes 6 hours
Is there a faster way to process 4 loads?
30
40
20
30
40
20
30
40
20
30
40
20
6 PM
7
8
9
10
11
Midnight
Time

## Slide 39: Laundry pipelining
Overlap the loads – start each new load as soon as possible, given available resources
6 PM
7
8
9
10
11
Midnight
Time
30
40
40
40
40
20
4 loads in 3.5 hours

## Slide 40: Pipelining terminology
Latency is the time from start to finish to wash one load of clothes
Throughput is the rate at which loads are completed
Pipelining does not decrease latency of any single load
Pipelining increases throughput when there is a collection of loads
Ideal technique? No Darn good? Yes
6 PM
7
8
9
Time
30
40
40
40
40
20
Latency
1 Thru

## Slide 41: Pipelining key characteristics
Pipelining does not improve execution time of a single task
Every subtask of the full task takes longer to execute than without pipelining because of
  slowest subtask in the pipeline delays faster subtasks
  possible dependence of one task on a previous task
Pipelining does increase throughput, the amount of work completed per unit time, because multiple tasks are being processed simultaneously
Result is reduced total time for a sequence of tasks
Workload comprised of many tasks is finished sooner because more work is being done simultaneously: there is more parallelism

## Slide 42: Pipelining a processor circuit
Hardware implementation technique whereby multiple instructions are overlapped in time
  Fetch-Execute cycle can iterate faster than any one instruction can complete
  Pipelining is the most basic processor speedup technique
Exploits parallelism (independence) among machine instructions, called instruction level parallelism (ILP)
  Easy for programmer to use because not visible to code
Hardware designer issues are
  Choose the number of stages
  Try for similar propagation delay for each pipeline stage
  Focus on throughput – rate of instruction completion

## Slide 43: Pipelined design (text Fig. 5.3)
Break the work for one instruction into stages
Change one-instruction-per-clock-cycle design to one-instruction-stage-per-clock-cycle
Overlap as many instructions as there are stages, ideally
Complete all stages every clock cycle, ideally
Non-ideal operation comes from
  Stage needs a bit string or a control signal that has not yet reached the stage or does not yet exist
  External memory cannot keep pace with stage circuits of the pipelined processor

## Slide 44: Combinatorial and Sequential circuits
Combinatorial circuits implement Boolean functions that are defined by truth tables
  Output = f(inputs); Inputs alone determine outputs
  No ability to retain a history of previous inputs
Sequential circuits implement finite state machines (computers) and are defined by next state diagrams
  Memory of all past sequential circuit inputs is represented by the current state, implemented as bits stored in a register
  Next state = f(current state, current inputs) where f( ) is a combinatorial function and circuit

## Slide 45: Sequential circuit viewed in time
Circuit transitions from one state to the next state, and so on
State i
State i+1
State i+2
f()
INPUTS
at time i
f()
INPUTS
at time i+1
• • •
Time
Register (collection of 1-bit memories) to hold current state
Combinatorial circuit to compute
next_state = f(current state, inputs)

## Slide 46: Sequential circuit for a pipeline state
Computation from preceding stage
Stage Register
Clock ___
Stage
combinatorial logic circuit computes f( )
__↑ Clock
Clock ↓____
Clock rising edge ↑ admits result bits into Stage Register Clock falling edge ↓ reveals these bits on Stage Register outputs, where these bits are now inputs for this stage
Clock falling edge ↓ starts the combinatorial logic computation
Previous result
Next result
f(Precious result)
f(Next result)

## Slide 47: The secret to completing instructions more rapidly? (Do less per clock cycle)
Break data & control paths into short segments, called stages
Stage starts with register of inputs to combinatorial circuits that compute result of that stage and pass to next register
Orange boxes are the pipeline registers
• Clock speed now limited only by the propagation delay within
the slowest stage, rather than propagation delay of entire circuit

## Slide 48: What does each stage do?
IF: Instr. fetch & next_PC
ID: Decode & reg. access
EX:
Execute
MEM: access
Data mem.
WB: Write back (result)
IF/ID
Reg.
ID/EX
Reg.
EX/MEM
Reg.
MEM/WB
Reg.
PC
Reg.

## Slide 49: Clocking the stage registers
Rising clock edge loads all stage registers with bits from preceding stage circuits, falling edge transfers these bits to register output, putting circuits of next stage to work

## Slide 50: Clocking the stage registers
Rising clock edge loads all stage registers with data from preceding combinatorial circuits, falling edge transfers data to register output, putting combinatorial circuits of next stage to work

## Slide 51: Lecture 20 – Addressing modes
2018.02.23
One of the things that is not so good is that a decision was made long ago about the size of an IP address - 32 bits. At the time it was a number much larger than anyone could imagine ever having that many computers but it turned out to be too small. – Jon Postel
known for RFC 791, RFC 792, and RFC 793

## Slide 52: Implications of implication
Implication means “it goes without saying,” which means no bits in the instruction bit string are required for this information
Using implication to specify the storage location(s)
  means that if other location(s) are desired for storing operand(s) and/or result(s) then a new opcode is required that implies it is paired with explicit location information
Using implication to specify
  the type of operand(s) and type of result(s) means that a change in data type requires a new operation definition and a new opcode
Notes: Examples: result(s) complex number math
A + B in a C program might be adding integers, might be adding floating point, cannot use same circuit, so the + in C will be translated to different instructions to the processor. The + is OVERLOADED.

## Slide 53: Instruction operands: How few is possible?
Each operand requires bits for either its immediate value or a pointer to operand
Immediate values are fast, but not necessary, so consider only # of pointers
Number of pointers (# of addresses) used in the instructions of actual ISAs:
  Zero, called a 0-address architecture
  One, 1-address architecture
  Two, 2-address architecture
  Three, 3-address architecture

## Slide 54: 0-address architecture: Stack machine
Operand locations are always implied, except
PUSH and POP instrs. have explicit operands
  PUSH and POP move operands between memory and a stack (of registers) within the processor
Instructions other than PUSH and POP take operand(s) from the stack, starting at the top, and place result on the new top of the stack
Example of a stack machine: a Reverse Polish Notation (RPN) calculator

## Slide 55: Code for C=A+B for 0-addr. machine
Assumes A, B, C all belong in memory and that A, B not destroyed
ALU
…
…
…
Processor
Top of
Stack 
Stack
Stack
Memory
Push A
Push B
Add
Pop C
Push A
A
A
B
Assembly instruction PUSH X copies the contents of memory location X into the Top of Stack register.
PUSH A uses the pointer A to point at a memory location, where the contents, also called A, are copied to the top of the stack.
Registers are used to construct the stack. They are too costly to use to construct all storage locations.
Memory is constructed of a different technology that is feasible to store a “large” number of bits.
Feasible can refer to many design parameters including money, heat, mass, volume, etc.

## Slide 56: Code for C=A+B for 0-addr. machine
Assumes A, B, C all belong in memory and that A, B not destroyed
ALU
…
…
…
Processor
Top of
Stack 
Stack
Stack
Push A
Push B
Add
Pop C
Memory
Push B
B
A
B
A
PUSH B copies B to the top of the stack.
A stack is a hardwired set of registers connected to perform the function of the stack data structure.
When an item is to be loaded into the stack Top position, all registers in the stack shift (load) their contents into the next lower register in the stack, making room at the TOP for the new item.
The number of registers in the Stack is a design choice.
If a stack is full, PUSH could drive the contents of the lowest stack register into the bit bucket – bad news for the program – so stacks include the ability to spill into memory.

## Slide 57: Code for C=A+B for 0-addr. machine
Assumes A, B, C all belong in memory and that A, B not destroyed
ALU
…
…
…
Processor
Top of
Stack 
Stack
Stack
Push A
Push B
Add
Pop C
Memory
Add
The ALU in a stack machine is hardwired to obtain two operands, one each from the Top of Stack register and the Next to Top register. Note the two arrows showing the paths from these registers to the ALU.
When the operation executes, the entire stack shifts its contents up one register level and the ALU output (operation result) is loaded into the Top register. Both operands in the stack are overwritten (bit bucket, again) as a side effect of execution, but copies remain in memory.
If the ALU operation is defined to use only one operand then the stack does not shift up and the result overwrites its own operand.
B
A
C
C
B
A

## Slide 58: Code for C=A+B for 0-addr. machine
Assumes A, B, C all belong in memory and that A, B not destroyed
ALU
…
…
…
Processor
Top of
Stack 
Stack
Stack
Push A
Push B
Add
Pop C
Memory
Pop C
C
B
A
Assembly instruction POP copies the contents of the Top of Stack register into a designated memory location AND causes the registers in the stack to all shift up a level, overwriting the current Top contents.
POP C uses the pointer C to point at a memory location and write into it the contents of Top of Stack, also called C.

## Slide 59: 1-address: Accumulator machine
One special register, called the accumulator
One operand for most instructions is the accumulator, one operand from a memory address
Result always sent to the accumulator; previous accumulator contents sent to the bit bucket
Example: cheap calculator

## Slide 60: 2-address machine
Not a stand-alone processor design
Rather, a design for an embedded memory copying circuit

## Slide 61: 3-address machine: current processors
Gain ability to specify location to store result
Avoid side effect of overwriting an operand
Machine code sequences to implement high-level language programs are more compact and faster
Register file is a design choice with the purpose of avoiding some use of slow main memory circuits

## Slide 62: Code for C=A+B for 0-, 1-, and 3-addr.
Assumes A, B, C all belong in memory and that A, B not destroyed
Reg-Reg/
Load-store
ALU
…
…
…
ALU
…
…
ALU
…
…
…
…
ALU
…
…
…
…
Processor
Top of
Stack 
Stack
Accumulator
Reg-Mem
Stack
Accum-ulator
Reg file
Reg file
Push A
Push B
Add
Pop C
Load A
Add B
Store C
Load R1,A
Add R4,R1,B
Store C,R4
Load R1,A
Load R2,B
Add R4,R2,R1
Store C,R4
Memory
C
B
A
C
B
A
C
B
A
C
B
A

## Slide 63: ISAs with dedicated instr. for mem access
0-address and Reg-Reg, a.k.a Load/Store, architectures have instructions specifically to read/write computer memory
3-address
Reg-Mem
Architecture
3-address
Reg-Reg/
Load-store Arch.
ALU
…
…
…
ALU
…
…
ALU
…
…
…
…
ALU
…
…
…
…
Processor
Top of
Stack
Memory
0-address
Stack architecture
1-address
Accumulator
Stack
Accum-ulator
Reg file
Reg file
Push
Pop
Load
Store

## Slide 64: Harvard architecture
Idea by Howard Aiken, Harvard physicist, to IBM Nov. 1937
Built by IBM in Endicott, NY and delivered to Harvard in Feb. 1944 as the Mark 1 computer
Has separate memories for program (instructions) and data
Input/output (I/O) to connect to the world
Processor to carry out the computations

## Slide 65: (John) Von Neumann architecture
Developed during his June 1945 train ride from Philadelphia to Los Alamos, NM
He had programmed Mark 1 in August 1944
One memory for both data and program
Same I/O, same processor as Aiken’s “Harvard” design
Notes: Von Neumann clearly better at social media than Aiken (Harvard vs Von Neumann architectures)

## Slide 66: Comparison of architectures
Harvard pro
  Can optimize one memory for storing data, other for storing program
  Can access data and program simultaneously
Harvard con
  Less flexible, memory is physically partitioned
Von Neumann pro
  Cheaper: each $ spent on memory helps store either data or program
  Less secure: hardware cannot distinguish between program instructions and data values

## Slide 67: Von Neumann bottleneck
Today, main memory technology (DRAM) is very slow compared to speed of a processor
  Processors consume operands and produce results far faster than current main memory technology can readily source and sink them
Time spent accessing memory often dominates the total time to run a program
Architects use the term von Neumann Bottleneck to describe the situation when memory access time (processor waiting) is the majority of the run time

## Slide 68: Operand addressing: immediate, direct, indirect
Operands can be found
  Within an instruction: immediate
  Within a register: direct (one HW pointing step using a register name (address) )
  Within memory: direct memory (one HW pointing step using a memory address; rare today)
  Within memory: indirect through a register (two pointing steps, first to register, then to memory; increasing the pointer size each step)
  Within memory: indirect memory reference (today, would combine indirect through a register followed by another level of indirection using the contents of the first memory location as a subsequent address; may repeat indirection)

## Slide 69: Example operand addressing modes (Fig. 7.6)
Notes: Thought question

## Slide 70: Design tradeoffs for operands
Different operand sources and forms have different
  Ease of programming/compiling
  Fewer/more machine instructions
  Smaller/larger machine instructions
  Larger/smaller range of immediate values
  Faster/slower operand fetch
  Larger/smaller processor circuit size
There is not one right answer

## Slide 71: Summary
Operand types and addressing are design choices
Immediate operands are constants contained within the instruction
Pointers to registers (smaller) and memory (often too large) are used in instructions
Can obtain operands via indirection
  Register contains an address to memory
  A memory location contains an address to memory