## Slide 1: Steps for debugging breadboard circuits
Verify power is on using LED on power rails
Hot component?
  Yes: There is always a nearby connection error; find it, fix it
  No:
    Using an LED to “see” voltage, test each node of your circuit design schematic for correct behavior
    Continue probing in breadth-first fashion until reaching a circuit graph node (vertex) where behavior is not as designed; there is a connection error here (colloquially called a wiring error); find it, fix it
    Also, reconsider design for correctness at each node
Connection error (wiring error) types and fixes are
  Device lead or wire goes to incorrect tie point; correct
  Wire is cracked in two inside the insulation, acting as an open switch; replace suspect wire with a known good wire, retest
  DIP package pin was bent and is not in the tie point; remove DIP, straighten pin, carefully re-insert, test circuit